INSPECTION, MAINTENANCE, AND USE OF THE BICYCLE RODEO TRAILER

This form offers instructions about how to use the bicycles, equipment, and trailer included in the Bicycle Rodeo Trailer in order to host a fun and safe bicycle rodeo.

INSPECTION

Before using any of the bicycles, equipment, or the trailer included in the Bicycle Trailer Rodeo, please inspect the items to make sure they appear to be in safe, working order.

Bicycles:

- Inspect that the tires are inflated to an appropriate pressure and do not have visible cuts or cracks. Also make sure tires have sufficient tread so that the user can brake safely and maintain control.

- Try spinning the wheels. Inspect that the wheels spin smoothly and straight. Inspect that there are no cracks or brakes in the the rims or spokes and that there are no missing spokes. Gently squeeze the rims to make sure they appear solid; move the rims from side to side to make sure they are not loose.

- Apply pressure downward, upward, rearward, and forward on the handlebars. Make sure the handle bars remain in the same position. Make sure that when you move the handlebars, the front wheel moves correctly.

- Inspect the body of the bike for any visible cracks or damage. Squeeze and feel the body of the bike to inspect for damage.

- Inspect the chain to make sure it is appropriately attached and oiled.

- Inspect the brakes by applying the brakes and pushing forward on the handlebars. Make sure the bike does not move.

- Inspect that the seat is securely attached and does not move: try moving it around.

Equipment:

- Visually inspect for any damage, such as tears, breakage, or missing parts.

- Inspect that any wearable equipment safely fits.

- Ensure that any signs are legible.

Trailer:

- Please see the “Bicycle Rodeo Trailer Towing & Check-Out Information Sheet” for instructions about inspecting the trailer.

**IF ANY BICYCLE, EQUIPMENT, OR TRAILER APPEARS DAMAGED, DO NOT USE IT!

USE

Bicycles:

- Make sure all bicyclists are appropriately supervised at all times.

- MAKE SURE ALL BICYCLISTS CORRECTLY WEAR HELMETS THAT FIT!

- Keep away from any vehicles.

- Do not use the bicycles during bad weather.

- Do not use the bicycles at night.

- Use the bicycles only on flat, even surfaces such as concrete or blacktop.

- Do not use the bicycles at fast speeds.

- Do not allow bicyclists to collide with one another.

- If the Bicycle Rodeo Trailer equipment is used to create a bicycling “obstacle course,” ensure that all bicyclists have been properly instructed about how to safely bicycle through the course before beginning.

- Immediately stop any bicyclist who seems to be bicycling in an unsafe way.

Equipment:

- Make sure any wearable equipment is correctly worn.

- Make sure “obstacle course” equipment is used in a safe way.

Trailer:

- Please see the “Bicycle Rodeo Trailer Towing & Check-Out Information Sheet” for instructions about use of the trailer.

- DO NOT TOW THE TRAILER IF IT IS UNSAFE TO TOW!

**DO NOT USE ANY BICYCLES, EQUIPMENT, OR TRAILERS IF THEY SEEM UNSAFE!

MAINTENANCE

Bicycles:

- If a bicycle requires maintenance, please do not attempt maintenance. Instead, place it aside and do not use it.

- Make sure that bicycles are used in ways that will prevent damage to the bicycles.

- Please make sure that the bicycles remain relatively clean.

- Make sure to store and supervise the bicycles so that they are not stolen or damaged. This may include keeping all unused bicycles in the trailer and supervising all use of the bicycles.

Equipment:

- If any piece of equipment requires maintenance, please do not attempt maintenance. Instead, place it aside and do not use it.

- Make sure that equipment is used in ways that will prevent damage to the equipment.

- Please make sure that the equipment remains relatively clean.

- Make sure to store and supervise the equipment so that it is not stolen or damaged. This may include keeping all unused equipment in the trailer and supervising all use of the equipment.

Trailer:

- Please see the “Bicycle Rodeo Trailer Towing & Check-Out Information Sheet” for instructions about maintenance of the trailer.

- If the trailer requires maintenance, please do not attempt maintenance. Instead, contact UHSO as instructed in the “Bicycle Rodeo Trailer Towing & Check-Out Information Sheet.”										Revised 2014